## Slide 1
Frozen residual-gated operator
Raw EDA
x
Normalize
x / scale
Stem
48 channels
Residual trunk
9 blocks · 48 channels
Dilations 1, 2, 4, 8, 16,
32, 64, 128, 256
Probability head
p = σ(logit)
Residual head
r = 4 tanh(d)
Gate
p × r
Robust scale
max(P95(raw) − P5(raw),
0.05 µS)
Normalized residual
max(x + p·r, 0)
normalized skip x
Output
residual × scale
scale path
Receptive field: 4089 samples ≈ 32 s at 128 Hz; VR input uses 58.8 Hz.
Notes: Residual-gated operator schematic in normalized coordinates. A 48-channel stem and nine dilated residual blocks feed probability and bounded residual heads. Their product modifies the normalized-input skip before nonnegative clamping and rescaling to physical conductance. The robust scale is the raw record/window 95th–5th percentile range with a 0.05 µS floor. The stated receptive field spans 4089 samples, approximately 32 s at 128 Hz; that duration does not transfer unchanged to 58.8 Hz VR data.
Native editable shapes; Arial, 6.5–7 pt labels and 8 pt panel letters. White background, minimal fills, no icons or decorative ruler. Original scientific labels and separate CRG-A / CRG-B identities retained.